Supercharger Installation Instructions

Mazda Rotary

The Camden Supercharger System utilizes a roots type supercharger developed specifically for automotive engine applications. The present supercharger design has evolved from the first Camden Supercharger built in 1956. The experience gained from hundreds of installations in circle track race cars, sports cars, passenger cars, trucks, marine, aviation and stationary engines has been applied to periodically upgrade the design for increased reliability and improved performance. Design features of the Camden Supercharger include extruded aluminum rotors with Teflon tip seals, pressure lubrication of the rotor shaft bearings, flanged pulleys for Micro-V drive belt, one piece front extension and multi ribbed rotor housings.

NOTE: This kit is not legal in California on emissions control vehicles.

Please take extreme care when working around fuel, due to the flammable nature. Do not smoke or work around open flames. Always wear safety glasses.

GENERAL INFORMATION

A supercharged engine when operating under boost, that is, with positive manifold pressure, will experience higher combustion pressures than a normally aspirated engine.  The effect is quite similar to raising the compression ratio.  The major difference is that a high compression engine experiences increased loads at all times whenever the engine is operating, while a low compression ratio supercharged engine encounters higher pressures only when under boost.  Most modern engines can withstand these increased pressures if proper consideration is given to fuel octane quality.  As with any high compression engine, supercharged engines require the highest octane fuel available to minimize any tendency towards destructive detonation.

Camden Superchargers recommend that boost be limited to 6 psi on an engine having a compression ratio of 8.5 to 1 when running on premium unleaded fuel of 92 octane.  If your engine has a lower compression ratio, it is possible to increase the boost.   Conversely, if your compression ratio is greater than 8.5 to 1, it will be necessary to reduce manifold pressure to prevent detonation.

If it is impractical to reduce the compression ratio of your engine to 8.5 to 1 or lower and you still want the performance gains associated with 6 psi boost, there are some options.  First of all, you could use higher octane fuel if it is available.  As an alternative, octane boosting additives are available, but their cost may make them unattractive for everyday use.  Boost retard systems are available, which automatically retard ignition timing as manifold pressure rises.  The major objection to these devices is as you retard timing you lose power.  The rationale appears to be that it is better to lose a little power under boost than to destroy an engine under detonation.  A type of boost retard can be accomplished by hooking the vacuum line from the distributor vacuum advance to the intake manifold.  This will assure no vacuum advance is occurring while under boost.

Another alternative which works well on borderline knocking engines is water injection.  A system which increases the volume of water is introduced as boost increases is commercially available and has proven to be quite effective in controlling detonation. However, just do not run out of water when you are under full boost.

Fuel mixture is extremely critical when operating under full boost as a lean mixture can lead to detonation.  A boost enrichment system can be added to provide a slightly richer mixture under full throttle, max boost operation.  The cooling effect of a rich mixture can prevent detonation under wide open throttle, full power conditions.  If managed properly, the slight loss of power due to excessive richness will hardly be noticed.

This supercharger kit has been designed specifically for the Mazda Rotary engine. Before installing the supercharger, you should verify that your engine is in good mechanical condition.   A compression test should be performed.   A supercharger should not be installed on an engine that is in poor condition or that has low oil pressure.

TOOLS AND EQUIPMENT REQUIRED FOR SUPERCHARGER INSTALLATION

Ratchet or speed handle, 3/8 drive

Torque wrench 100 lb-ft. capacity

Socket set; 3/8 drive Metric and U.S.

Extensions: 3” & 6”.

8” vise grips

10” adjustable wrench

End wrenches, Metric and U.S.

7/16” drill bit with drill motor

Gasket scraper

Straight blade screwdriver

Pliers

RTV Silicone (Permatex Ultrablue)

¼” NPT tap and tap handle

TORQUE VALUES

Blower hold down bolts						18 lb-ft

Inlet Manifold, nut and bolts					13.5 - 20 lb-ft

INSTALLATION

NOTE: Supercharger rotors have very close operating tolerances between themselves and the rotor housing. Any foreign object introduced through the carburetor flange opening can cause serious damage to the internal components.  Keep the protective tape on both the inlet and discharge ports until the last possible moment.

| 1. | Remove the stock intake manifold, crankshaft pulley, water pump pulley, and alternator pulley. Install the new water pump pulley and alternator pulley. Clean the face of the crankshaft hub of all grease and foreign matter, and then install the supercharger crank pulley with the four stock screws. Be sure to transfer your timing mark to the new crank pulley. If belt driven accessories, such as power steering and air conditioner are used, install the stock accessory pulley(s) in front of the new crank pulley. |
| --- | --- |
| 2. | Remove the oil filter and oil filter stand. Install the new oil filter stand provided using the new O rings provided. |
| 3. | Remove the oil pan. Drill a 7/16" hole through the front cover and tap for ¼” NPT. To gain access you may need to remove the oil metering pump and water pump housing. Clean all metal chips to avoid contamination of oil system. |
| 4. | Install the 45˚ ½” push lock to ¼” NPT into the tapped hole in the front cover as shown below. Reinstall the oil pan using RTV sealant as the gasket. Reinstall water pump housing and the oil metering pump using new gaskets (if necessary). |
| 5. | Install the supercharger assembly using the new inlet manifold gasket provided and the stock bolts. If a boost gauge is to be used, install the boost gauge line in the 1/8” NPT threaded hole at the rear of the manifold. If not using a boost gauge you will need to install a 1/8" NPT plug. |
| 6. | Install the ½” drain hose between the front fitting of the supercharger and the newly installed 45˚ elbow. Clamp the hose using the hose clamps provided. |
| 7. | Install the oil feed assembly to the rear “T” fitting of the supercharger and install the opposite end to the rear of the oil filter stand 90˚ fitting as shown below. |
| 8. | Install the idler pulley mount to engine using the three bolts provided. Install the idler pulley using the 3/8” bolt and washer. Torque to 18 ft-lb. |
| 9. | Install belt. Adjust belt tension using the alternator. The belt is tensioned properly when a 20 pound force applied mid span on the tension strand of the belt results in a deflection of ½”. |
| 10. | Install the carburetor of your choice. We recommend the Holley 650cfm double pumper. |
|  | Wire Oil Metering Pump to 9 O’Clock. |
| 11. | Start the engine and adjust the carburetor for a smooth fast idle. Allow the engine to run for about 15 minutes to assure that lubricating oil has circulated through the supercharger. Check for oil leaks. DO NOT CRANK ON THE ENGINE FOR EXTENDED PERIODS OF TIME WITHOUT STARTING AS THIS CAN DRY OUT THE BEARING SURFACES INSIDE YOUR CAMDEN SUPERCHARGER. |
| 12. | Install a suitable air cleaner and secure any loose wires or hoses to tidy up the installation. |

Congratulations!!!  You have just completed a Camden Supercharger installation.  Now go out and enjoy the increased performance, but remember you now have a lot more torque available so use caution, particularly in low gear, to avoid excessive wheel spin or over-revving your engine.

Camden Superchargers is continually upgrading products with new capabilities or product improvements.  Many of these changes are made possible by valuable and informative recommendations from our customers.  If you wish to contact Camden with recommendations or just to let us know how your installation turned out, give us a call or write to us at:

Camden Superchargers / Atkins Rotary

16715 Meridian East, Building K-A

Puyallup, WA 98375

(253) 848-7776

Warranty

Nature and Duration of Warranty
Camden Superchargers, (hereinafter “Seller”) warrants to the buyer that products sold under this order shall, on the date of retail purchase and for twelve (12) months thereafter, conform to the Specifications and Drawings referenced in the order and be free from defects in materials and workmanship.  Buyer’s sole remedy and seller’s sole liability, under this warranty, shall be at the seller’s option.  Repair, replacement, or refund of the purchase price of any such product is based upon examination by seller or seller’s designee, and the determination that, to seller’s reasonable satisfaction, to have be nonconforming or defective.  Repaired or replaced products are warranted only for the remaining unexpired portion of the original warranty.

Sole Warranty 
This warranty is in lieu of all other warranties, expressed or implied, including, without limitation, any warranties of merchantability or fitness for a particular purpose. All such other warranties are hereby disclaimed and excluded by seller. In no event shall the seller be liable for any special incidental, or consequential damages with respect to seller’s performance or non-performance of this order or products delivered hereunder.

Procedure
Before returning a product for warranty service, buyer should obtain shipping instructions and a Return Authorization Number (RAN) from Camden Superchargers, (253) 848-7776, 16715 Meridian E, Bldg K-A, Puyallup, WA  98375.  Buyer shall pay the cost of transportation both ways for warranty services.

Warranty Limitations 
The warranty, provided in Paragraph 1, shall not apply to any product that has been subject to misuse, neglect, accident, improper application, (see Warranty Limitations), or exposure to an environment beyond the limits described in the Specifications.  The warranty shall not apply to any product that has been altered or repaired outside of seller’s written consent.  Also, the warranty shall not apply to anyone other than the buyer without seller’s prior written consent.

The Camden Supercharger Warranty does not cover the following:

1.    Normal wear and tear.
 2.    Damage resulting from improper oil or lack of oil.
 3.    Damage to related components, i.e. engine, drive train.
 4.    Costs due to down time or towing.
 5.    Shipping costs.
 6.    Removal or replacement costs.
 7.    Damage resulting from foreign object ingestion.
 8.    Damage resulting from improper installation.
 9.    Damage resulting from any misuse or abuse.
10.    Any product used for racing or competition.
11.    Any supercharger used with a crank speed to blower speed drive ratio of greater than 2.
12.   Any supercharger used to produce boost levels of greater than 10 psi.
13.   Supercharger damage due to backfire.